## Slide 1
Avgi Kollakidou avko@mmmi.sdu.dk
PhD Student
SDU Robotics, Maersk Mc-Kinney Moller Institute
Gazebo
Robots in Context
October 2023

## Slide 2: General
Tutorial links on bottom of each page
Commands indicated by: $ command
Each ROS command is launched in a new terminal
Variables that should be changed indicated by: <> ($ros2 topic echo <topic>)

## Slide 3: Content
Gazebo
  What is Gazebo?
  Why Gazebo?
  RViz vs Gazebo
  Gazebo Elements
Transformations TF2
Universal Robot Description Format
Programming exercise

## Slide 4: Gazebo

## Slide 5: What is Gazebo?
Simulation engine
Realistic rendering of environments
Multiple physics engines
    ODE – default [1]
    Bullet [2]
    Simbody [3]
    DART [4]
​[1] Open Dynamics Engine - https://www.ode.org/​ [2] Bullet - https://pybullet.org/wordpress/
[3] Simbody - https://simtk.org/projects/simbody [4]Dynamic Anumation and Robotics Toolkit https://dartsim.github.io/

## Slide 6: Why Simulation?
Save time
Hardware independent
Cheap failures

## Slide 7: Why Gazebo?
3D physics and dynamics
Configurable
User interaction
Large community
  robot models
  sensors (noise)
ROS compatible

## Slide 8: Gazebo vs RViz
Simulate
environment
sensors
physics
Visualise
surroundings
sensor readings
Robot equipped with
camera
laser scanner

## Slide 9: RViz vs Gazebo (vs rqt)
GUI for ROS
Transformation tree
Dynamic reconfigure
Topic graph
Image viewer

## Slide 10: Gazebo Architecture
Server
  simulating the physics, rendering, and sensors
Client
  visualise and interact with simulation
https://classic.gazebosim.org/tutorials?tut=architecture&cat=get_started#Introduction

## Slide 11: Launch Gazebo
Independent
$ gzserver
$ gzclient
$ gazebo
With ROS
$ ros2 run gazebo_ros gazebo
$ ros2 launch gazebo_ros <world_name>.launch
Empty world - turtlebot

## Slide 12: Gazebo Elements
Worlds
  robots and objects (buildings, tables) & global parameters (sky, ambient light)
Models
  links, joints, sensors, plugins
Links
  visual objects -- define visual representation
  collision objects -- define colliding surface
Joints
Sensors
Plugins
Notes: All collections of something
World – collection of robots
Model – collection of links ...

## Slide 13: Worlds
Collection of worlds - https://github.com/chaolmu/gazebo_models_worlds_collection
Gazebo world tutorial - https://classic.gazebosim.org/tutorials?tut=build_world&ver=1.9
Collection of models
Launched by gzserver
'.world' file
URDF (Unified Robot Description Format)
SDF (Simulation Description Format)

## Slide 14: Models
Collection of models - https://github.com/osrf/gazebo_models
Gazebo model tutorial - https://classic.gazebosim.org/tutorials?tut=build_model&cat=build_robot
Physical properties:
  Body – simple shapes
  Kinematics
  Dynamics
  Appearance
Interface
Husky - Clearpath
Simple robot – bunchOfCoders
Notes: Kinematics: joints, velocities
Dynamics: mas, friction, forces

## Slide 15: Links
Physical properties:
  Body – simple shapes
  Kinematics
  Dynamics
  Appearance
Interface
Notes: Kinematics: joints, velocities
Dynamics: mas, friction, forces
Interface for control

## Slide 16: Joints
URDF
Revolute -- hinge joint, limited range
Continuous -- hinge joint, no limits
Prismatic -- sliding joint, limited range
Fixed -- all degrees of freedom locked
Floating -- allows motion for all 6 DOF
Planar -- allows motion
URDF links - https://wiki.ros.org/urdf/XML/joint
SDF links - http://sdformat.org/spec?ver=1.9&elem=joint#joint_type
Notes: Kinematics: joints, velocities
Dynamics: mas, friction, forces
Interface for control

## Slide 17: Sensors
Contact
Camera
GPS
IMU
Ray (range data)
...
Notes: Kinematics: joints, velocities
Dynamics: mas, friction, forces
Interface for control

## Slide 18: Links & Joints

## Slide 19: Links & Joints

## Slide 20: Links & Joints

## Slide 21: Links & Joints

## Slide 22: Links & Joints

## Slide 23: Frames & Transforms

## Slide 24: TF2

## Slide 25: TF2
Static transforms:
Wheel – base
Camera – base
End-effector – link

## Slide 26: TF2

## Slide 27: TF2
View TF frames information
$ ros2 run tf2_tools view_frames
Real time information
$ ros2 run tf2_ros tf2_echo [source_frame] [target_frame]
Play data:
$ros2 bag play <bag_name>
The data can then be viewed in Rviz

## Slide 28: TF2
Frames for:
Object detection with laser scanner?
People tracking from camera?

## Slide 29: URDF

## Slide 30: URDF
XML
Textual CAD
Description of shapes, locations and connections of parts
Used by:
  RViz – visualise robot
  Gazebo – simulate robot
  Navigation Stack – move around properly
https://industrial-training-master.readthedocs.io/en/melodic/_source/session3/Intro-to-URDF.html
http://wiki.ros.org/urdf/Tutorials/Building%20a%20Visual%20Robot%20Model%20with%20URDF%20from%20Scratch

## Slide 31: URDF vs SDF
URDF
ROS compatible
Simple model descriptions
  robots
  sensors
SDF
Gazebo compatible
Extra features
World description
URDF --> SDF compatibility

## Slide 32: Main elements
Link – rigid body
Joint – connection of 2 links

## Slide 33: Links
Visual
name
Collision
geometry
origin
geometry
origin
Material
Inertial
origin
mass
inertia
https://wiki.ros.org/urdf/XML/link

## Slide 34: Joints
Attributes
name
type
Elements
origin
axis
calibration
dynamics
mimic
safety_controller
parent
child
limit (prismatic/revolute)
https://wiki.ros.org/urdf/XML/joint

## Slide 35: Links - Geometry
Shape | Declaration
Cylinder | <cylinder length="" radius=""/>
Box | <box size="x y z"/>
Sphere | <sphere radius=""/>
Mesh | <mesh filename=""/>

## Slide 36: Links Material & Origin
MATERIAL
<material name="">
  <color rgba="R G B α"/>
      (Values between [0 1])
</material>
<material name="">
  <texture filename=""/>
</material>
ORIGIN
<origin rpy="r p y" xyz="x y z"/>
rpy: roll, pitch and yaw of fixed axis in radians.
xyz: location offset
(defaults to identity if not specified)

## Slide 37: Links Inertia & Mass
Inertia
<inertia ixx="" ixy="" ixz="" iyy="" iyz="" izz="" />
Mass
<mass value=""/> (kg)

## Slide 38: Joints
<parent link=""/> <child link=""/>
<limit
effort="" velocity="" lower="" upper="" />
Effort: N or N/m
Velocity: m/s or rad/s
<axis xyz=""/>
Axis of rotation or translation
<dynamics damping="" friction=""/>
+more

## Slide 39: Visual vs Collision
Visual
More complex
Include meshes
Colours
Materials
No effect on physical properties!
Collision
Simple shapes
  Collision detection computationally simpler
Define safety zones
  Slightly larger areas for avoiding contact

## Slide 40: Make a robot model

## Slide 41: Links
Body – cylinder
Right Leg - box
Left Leg - box

## Slide 42: Examine your URDF file
Syntax check
  $ check_urdf <filename>.urdf
Graphical representation of link structure
  $ urdf_to_graphiz <filename>.urdf
View in RViz
  $ roslaunch urdf_tutorial display.launch model:=<filename>.urdf
requires: $ sudo apt-get install ros-humble-urdf-tutorial

## Slide 43: Programming Exercise
Version 1 – mobile robot
  Model a mobile robot using URDF (differential drive suggested)
  Visualise in RViz
  Spawn model in Gazebo
  Mount camera or laser scanner on robot
  Visualise sensor data

## Slide 44: Programming Exercise
Version 2 – manipulator
  Model a manipulator arm using URDF (minimum 2 joints)
  Visualise in RViz
  Spawn model in Gazebo
  Mount camera on robot end-effector
  Visualise sensor data

## Slide 45: PRACTICAL

## Slide 46: Terminator
  $ sudo apt-get install terminator

## Slide 47: ROSBAG

## Slide 48: Rosbags
Simple recordings of sensor data
Easy way into understanding ROS, topics and messages
Replay your experiments
  Find issues
  Review data
  Share data

## Slide 49: Commands
Record data:
$ros2 bag record <topic_name1> <topic_name2>
View data info:
$ros2 bag info <bag_name>
Play data:
$ros2 bag play <bag_name>
The data can then be viewed in Rviz

## Slide 50: Export rosbag data
$ros2 bag play <bag_name>
$ros2 topic echo <topic_name> > data.csv

## Slide 51: Read data with Python (or any other language)

## Slide 52: Download Gazebo
We will use Gazebo Fortress
$ sudo apt-get install ros-humble-ros-gz